--HLOGIT.DOC------------------------------------------------------------

  HIERARCHICAL CHOICE MODELS: THREE LEVEL NESTED MULTINOMIAL LOGIT
  ================================================================

  COPYRIGHT (C) AXEL BOERSCH-SUPAN.  ALL RIGHTS RESERVED.

  PROGRAM (VERSION 6.2):  NOV 29, 1989
  Documentation Update:   FEB 16, 1990

-----------------------------------------------------------------------

  1. INTRODUCTION
  ===============

  1.1  GENERAL DESCRIPTION:
  =========================

This program analyses the nested multinomial logit model (NMNL) or
hierarchical decision tree with up to three levels.

In particular, HLOGIT will

  -  Define and display any one to three-level tree structure;
  -  Check the data and calculate sample means and frequencies;
  -  Generate interactions between variables and alternatives;
  -  Weight observations for grouped data estimation;
  -  Allow for choice based sampling (WESML);
  -  Support unbalanced choice sets;
  -  Support any parameter equality restrictions;
 
  -  Maximize the full information likelihood function;
 
  -  Predict market shares and compute prediction success table;
  -  Calculate the covariance matrix correcting for WESML sampling;
  -  Calculate elasticities of choice probabilities;
  -  Test the significance of the tree structure;
  -  Compute implied correlation matrix of unobserved utility components.


The Program runs as batch-program or interactively.  In the latter case, there
is a menu-display before each operation and you will be prompted for options at
various stages of the program.  See Chapter 3 for details.


The user has to provide three input files

   "HLOGIT.PRO" (explained in Section 2.1):
        Profile with default values.  In batch mode, commands are appended.

   "INPARMS.PAR" (explained in Section 2.2):
        Dimensions, tree structure, parameter labels, and initialvalues.

   "INDATA.DAT" or "INDATA.BIN" (explained in Section 2.3):
        Data (dependent and explanatory variables by alternative) in 
        ASCII or binary form.

In interactive mode, the terminal will prompt for actual file names.
A blank name is interpreted as usage of the default names specified in
"HLOGIT.PRO" which will also be used in batch mode.

Results will be printed on the terminal screen.  They can also be echoed
("spooled") on a file using the spool option.  In addition, the estimated
parameters are always written on a file that has the same structure as
"INPARMS.PAR" and can therefore be used as input at a later stage.

---------------------------------------------------------------------------

  1.2. ECONOMETRIC SPECIFICATION AND NOTATION
  ===========================================

As an example for notation and terminology, consider the following NMNL
model symbolized by a decision tree:


  Level 0: (stem)                                   |
                                           +--------þ--------+
  Level 1: (limbs)                         1                 2
                                           |                 |
     Upper-level dissimilarity coeff.     (ç)           +---(ç)-------+
                                           |            |             |
  Level 2: (branches)                      11           21            22
                                           |            |             |
     Lower-level dissimilarity coeff.    +[é]+     +-+-[é]-+-+     +-[é]-+
                                         | | |     | | | | | |     | | | |
  Level 3: (twigs)                       | | |     | | | | | |     | | | |
                                         | | |     | | | | | |     | | | |
     Elemental Alternatives:             1 2 3     4 5 6 7 8 9     0 A B C


This tree has two limbs.  The first limb has one upper-level dissimilarity
parameter (c,).  This dissimilarity parameter is called "trivial" because
the limb has only one branch.  This branch has one (non-trivial) lower-
level dissimilarity parameter (e') and three elemental alternatives.
The second limb has one (non-trivial) upper-level dissimilarity parameter
(c,) and two branches.  Each of these branches has one (non-trivial) lower-
level dissimilarity parameter (e').  The first branch has six, the second
branch four elemental alternatives.

We will employ a short-hand notation for trees consisting of numbers and
letters symbolizing elemental alternatives, separated by commas and semi-
colons to denote the structure of branches and limbs.  Semicolons separate
limbs, commas separate branches from each other.

The above tree will be denoted by the string  123;456789,0ABC  because
alternatives 1-3 are on a different limb as alternatives 4-C and alter-
natives 4-9 on a different branch as alternatives 0-C.
The corresponding MNL model would be simply a string of all 13 alter-
natives:  1234567890ABC.

Alternatives are labeled by numbers and letters as follows:
Labels 1-9 for alternatives 1-9
Label  0   for alternative  10
Labels A-Z for alternatives 11-36


  LIKELIHOOD FUNCTION:
  --------------------

The NMNL model is characterized by the likelihood function

   L = log { P(T|B,L) * P(B|L) * P(L) } , where


   T=chosen twig, B=chosen branch, L=chosen limb

   P(T|B,L) = exp { X(L,B,T)*BETA/THETA(L,B) } / exp { INC2(L,B) }

           where INC2(L,B) = log  a"  exp { X(L,B,T')*BETA/THETA(L,B) }
                                T'i^ B
                                B i^ L

  P(B|L) = exp { INC2(B)*THETA(L,B)/TAU(L) } / exp { INC1(L) }

           where INC1(L) = log  a"  exp { INC2(B')*THETA(L,B')/TAU(L) }
                              B'i^ L

  P(L) = exp { INC1(L)*TAU(L) } / exp { INC0 }

           where INC0 = log  a"  exp { INC1(L')*TAU(L') }
                             L'

NOTE:  We employ the so-called "discrete choice formulation" in which
=====  the parameters BETA are constant across alternatives.

IMPORTANT: To be identified, the corresponding variables X(L,B,T)
  must exhibit at least some variation across alternatives
  ("constant-BETA/varying-X description").
  Handling of agent-specific characteristics that do not vary across
  alternatives is discussed in Section 1.3 on the interaction feature.

---------------------------------------------------------------------------

  1.3  THE INTERACTION FEATURE
  ============================

A user should be aware that discrete choice models can include two different kinds of explanatory variables:

 - variables that vary across alternatives ("alternative-specific attributes")

 - variables that are constant across alternatives and characterize the
   decision-making agent ("agent-specific characteristics")

HLOGIT provides a convenient way to interact alternatives and both kinds of
explanatory variables.  All variables can interact with one or more dummy variables that characterize certain alternatives.  This is particularly relevant for agent-specific characteristics, i.e., those variables that do not vary across alternatives.  This is for the following reason:

The choice among a finite set of discrete alternatives is governed by the
DIFFERENCES among the alternatives, not the ABSOLUTE LEVEL of their
attributes.  Attributes that are constant across alternatives do not
differentiate the alternatives, they are thus irrelevant for the choice
among them.  Coefficients associated with constant attributes cannot be
identified.

However, agent-specific characteristics may affect different alternatives
in different ways.  In other words, there is an interaction effect
between this agent-specific characteristic and some alternatives RELATIVE
to other alternatives.  In order to identify agent-specific characteristics
it is therefore necessary to interact agent-specific characteristics
with dummy variables that are turned on in some alternatives and turned off
in others.

Variables that vary across alternatives ("alternative-specific attributes")
are identified without such interaction terms.  Sometimes, however, a user
may estimate different coefficients for different (groups of) alternatives.
Again, this amounts to interacting these variables with dummies that are
specific to certain alternatives.

HLOGIT provides a map for each variable (including the constant term) in
which these interactions must be specified.  For each variable K, the
map consists of the number of interaction terms, NXM(K), and an array
LMAP(K,I,M) that defines whether dummy variable M, M=1,..,NXM(K) is turned
on in alternative I, I=1,..,NALT, the number of alternatives.

It is helpful to distinguish the following three cases:


(CASE 1) NO INTERACTION:
------------------------
NXM(K)=1,  LMAP(K,I,1)=1   for all alternatives I=1,..,NALT

EXAMPLE for NALT=6:     NXM=1      LMAP=1 1 1 1 1 1

In this case, one common coefficient for all alternatives is associated
with variable K.  This coefficient will only be identified, if variable K
exhibits variation across alternatives.  This is the standard case for
alternative-specific attributes that vary across alternatives (like travel
time in transportation mode choice)


(CASE 2) STANDARD INTERACTION:
------------------------------
NXM(K)=NALT-1     LMAP(K,I,M)=1   if I=M      I=1,..,NALT; M=1,..,NALT-1
                              0   else

EXAMPLE for NALT=6:     NXM=5      LMAP=1 0 0 0 0 0
                                        0 1 0 0 0 0
                                        0 0 1 0 0 0
                                        0 0 0 1 0 0
                                        0 0 0 0 1 0

In this case, NALT-1 constants will be assigned to each elemental
alternative except one (here: the last one).  NALT-1 coefficients will be
estimated for variable K, each measuring the effect of this variable on a
single elemental alternative relative to the omitted (here: last)
alternative.  This is the standard case for agent-specific characteristics
that exhibit no  variation across alternatives (like income in mode choice).


     (A BRIEF NOTE ON THE SPECIFICATION OF DISCRETE CHOICE MODELS:
     
        HLOGIT adopts the "constant-BETA/varying-X" formulation of discrete
        choice models in the above likelihood function. For variables that
        does not vary across alternatives, the standard interaction with
        NALT-1 dummies replaces
             X(L,B,T)*BETA
        in the above "constant-BETA/varying-X" likelihood function by the
        interactions
             [X*DUMMY(L,B,T)]*BETA = X*[DUMMY(L,B,T)*BETA].
        This is evidently equivalent to estimating a "constant-X/varying-BETA"
        likelihood function with
              X*BETA(L,B,T)
        in the place of X(L,B,T)*BETA.)


(CASE 3) USER-SPECIFIED INTERACTIONS:
-------------------------------------
Instead of assigning NALT-1 dummies where each dummy corresponds to
exactly one alternative, one may want to assign a set of NXM(K)óNALT-1
dummies where each dummy may represent one or more alternatives.  In this
case, NXM(K) coefficients will be estimated for each variable K.

NOTE: This procedure amounts to placing simple linear restrictions
      on the standard interactions in CASE 2.

NOTE: This procedure is particularly useful for a symmetric tree
      where the alternatives have a factorial structure, that is,
      each limb has the same number and kind of branches, and each branch
      has the same number and kind of alternatives.  In this case,
      (number of limbs-1)+(number of branches per limb-1)+(number of
      alternatives per branch-1) constants will be assigned, implying an
      assignment of less than NALT-1 constants, therefore a substantial
      saving in the number of explanatory variables.

NOTE: In the case of variables that do not vary across alternatives, the
      user should of course be careful that the dummies do not add up to one.

EXAMPLES for NALT=6, TREE=12,3;45,6:

      a) NXM=3    LMAP=1 1 1 0 0 0
                       1 1 0 1 1 0
                       1 0 0 1 0 0

         In this example, dummy 1 characterizes the first limb,
         dummy 2 the first branch in each limb, and dummy 3 the
         first alternative in branches 11 and 21.  The first coefficient
         of each agent-specific characteristic describes the effect of
         that characteristic on all alternatives in the first limb.
         The second coefficient of each agent-specific characteristic
         describes the effect of that characteristic on the alternatives
         in the first branches in each limb.  The third coefficient of 
         each agent-specific characteristis describes the effect of that
         characteristic on the first alternatives in each limb.  All
         effects are relative to the last alternative.


      b) NXM=4    LMAP=1 1 1 0 0 0
                       1 1 0 0 0 0
                       0 0 0 1 1 0
                       1 0 0 0 0 0

         In this example, dummy 1 characterizes the first
         limb, dummy 2 the first branch in limb 1, dummy 3 the
         first branch in limb 2, and dummy 4 alternative 1 only.


NOTE:  See also the example in data section 2.3 that shows the correspondence
=====  between raw data (without interactions) and expanded data (interacted).

-----------------------------------------------------------------------------


  2. USAGE OF HLOGIT
  ==================

HLOGIT can be called in four ways from the DOS-prompt:

  C:>HLOGIT
  C:>HLOGIT MYPROFIL.TXT
  C:>HLOGIT /B
  C:>HLOGIT /B MYPROFIL.TXT

The first two calls invoke the interactive version of HLOGIT, the last two
calls invoke the batch version. Calls 1 and 3 use the standard profile with name
HLOGIT.PRO.  Calls 2 and 4 use a user-defined profile with name MYPROFIL.TXT.

The following sections describe the three input data sets "HLOGIT.PRO",
"INPARMS.PAR", and "INDATA.DAT/BIN" that must be present for HLOGIT.


-----------------------------------------------------------------------------


  2.1  THE PROFILE "HLOGIT.PRO":
  ==============================


The profile contains the default values for parameters and filenames.
If no profile is specified in the command line, HLOGIT uses the default
profile with the name HLOGIT.PRO.

In interactive mode, the profile defines the default values of data handling
and optimization which may be overridden in the actual prompts.

In batch mode, the profile contains the actual values of data set names and the
batch commands.


The profile contains at least 11 lines.  The first line is a header which is
ignored by the program.  In the following 10 lines, 10 default values are
attached to 10 keywords:

    keyword:  value:       default for:
    scr_pause=5            length of pause (in seconds) between screens
    max_obs  =0            maximum number of observation (0=EOF or buffer size)
    data_mode=0            data mode: 0=ascii, 1=binary, 2=ascii&binary scratch
    max_iter =10           iteration limit for optimizer
    accuracy =0.001        accuracy for optimizer
    optimizer=2            algorithm for optimizer
    param_in =hltest.par   file name for parameter input file
    data_in  =hltest.dat   file name for data input file
    spool_out=hltest.spo   file name for spool output file (blank=none)
    param_out=hltest.out   file name for parameter output file

Do not change the order of the lines, and start each input in column 11,
as shown above.  Comments are allowed past column 21, except for the last
four rows of filenames which may be up to 40 characters long.

scr_pause: Length of pause (in seconds) between screens in interactive mode.
           0 or smaller: no pause
           1-59: pause in seconds
           60 or larger: prompt between screens
           (In batch mode, scr_pause is ignored.)

max_obs:   Number of observations used in estimation.
           0 denotes as many observations as the internal workspace will hold.
           If the actual data set is smaller than any of the above, the entire
           data set is used.

data_mode: type of data set, see Section 2.3

max_iter, accuracy, optimizer:  iteration limit, accuracy and algorithm of
           optimaization routine, see Section 3.1

param_in:  default name for input parameter file "INPARMS.PAR".  Must be
           present.  See Section 2.2

data_in:   default name for data input file "INDATA.DAT".  Must be
           present.  See Section 2.3

spool_out: default name for spool output file.  Optional.  If not blank,
           all screen-output is also echoed to this file.  See Section 3.12.

param_out: default name for parameter output file "OUTPARMS.PAR".  Must be
           present.  See Section 3.20


In batch mode, the profile then contains (starting in line 12) the batch
commands described in Section 3.  See HLDEMO.PRO for an example of a profile
which includes batch commands, and HLOGIT.PRO for an example of a standard
profile without batch commands.


-----------------------------------------------------------------------------


  2.2  TREE-SPECIFICATION AND INITIAL-VALUES: THE INPUT FILE "INPARMS.PAR":
  ========================================================================

     This file contains
     A) the functional form of the decision-tree,
        i.e., the arrangement of the alternatives in the tree,
     B) the number of explanatory variables,
     C) the interactions for each explanatory variable,
     D) and the initialvalues for the parameters.

     Input lines are marked by in the sequal by ">>>>>" in the margin.
     They are read by list-directed I/O (*-format).  Therefore, inputs must
     be separated by a comma and/or at least one blank space.


     A) TREE STRUCTURE   [format 72A1]

>>>>>   STRUCT(1,...,72)

        The tree structure is denoted by the string STRUCT of up to 72 
        characters.  Numbers 1-9, 0, then letters A-Z in this string symbolize
        the elemental alternatives in that order.
        Semicolons separate limbs, commas separate branches from each other.
        See the example at the top of this file and the test program at the
        bottom of this file to get familiar with this notation.

        NOTE: HLOGIT checks the level of the tree by counting
              commas and semicolons in the TREE string.
              Case 1: If there is at least one semicolon, the full three-level
                      code is used.
              Case 2: If there is at least one comma, but no semicolon, the
                      quicker two-level code is used.
              Case 3: If there is neither a comma nor a semicolon, simple MNL
                      is applied.
              The number of alternatives is computed as the number of non-blank
              characters in STRUCT that are not commas or semicolons.

        NOTE: The order of the alternatives in STRUCT is significant and can
              be different from 1-9,0,A-Z. The data, however, must always be
              in ascending order 1-9,0,A-Z.  Also any other input in this file
              refers to the alternatives in ascending order, not the actual
              order specified in STRUCT.  The only exception are the initial
              values for the dissimilarity parameters which refer to the actual
              order as specified in STRRUCT, see below.


     B) NUMBER OF EXPLANATORY VARIABLES  [*-format]

>>>>>   NX, NXD, NXA, NWT, NCS

        where NX  = number of alternative-specific attributes
                      (these variables vary across alternatives)
              NXD = number of agent-specific characteristics
                      (these variables do not vary across alternatives and
                       must interact with at least one dummy that varies
                       across alternatives).
              NXA = 0 if a constant should not be included.
                  = 1 if a constant should be included,
                      (the constant does not vary across alternatives and
                       must interact with at least one dummy that varies
                       across alternatives).
              NWT = 0 if each observation has the same weight,
                  = 1 if weights are included,
              NCS = 0 if each observation has the same choice set.
                  = 1 if a choice set variable is included,


        NOTE: NX, NXD refer to the number of variables read from the data file.
              Do not count interactions, and do not distinguish between those
              variables that are associated with coefficients that will be
              estimated freely and those with equality-constrained coefficients.

        NOTE: Cf. Subsection 2.3.2, Variable Types, for further discussion.


     C) INTERACTIONS  [*-format]

>>>>>   For each variable K = 1 through NX+NXD+NXA:
>>>>>
>>>>>   NXM(K)     LMAP(K,1,1)  , ... ,LMAP(K,NALT,1)
>>>>>              ...
>>>>>              LMAP(K,1,NXM), ... ,LMAP(K,NALT,NXM)

        where NXM(K)      = number of dummy variables interacting with
                                  variable K
              LMAP(K,I,M) = 1 if the M-th dummy for variable K is turned on
                                  in alternative I,
                            0 if turned off.


        NOTE: See Section 1.3 for examples.

        NOTE: The order of variables K as well as the order of alternatives I
              in LMAP has to correspond to the order of the variables and the
              alternatives in the data.  Specifically, the first NXM(1) rows
              in LMAP relate to the first variable, the second NXM(2) rows
              relate to the second variable, etc.  Similarly, the first column
              in LMAP relates to alternative labeled 1, the second column
              relates to alternative labeled 2, etc.

        NOTE: The total number of lines in the maps for all variables has to
              be equal to the number of initial values for all parameters
              (excl. dissimilarity parameters), NXX.  NXX is the sum of
              NXM(K) for all K=1,..,NX+NXD+NXA, i.e., the number of all
              interactions (incl. the trivial ones) of all explanantory
              variables (alternative-specific variables, agent-specific
              variables and alternative-specific constants).


     D) INITIAL VALUES  [format (A8,1X,I1,F15.9) ]

>>>>>   For each parameter J=1,..,NPP:
>>>>>
>>>>>   column 1...8:   column 10:   column 11...24:
>>>>>
>>>>>   NAME( 1)        ISTAT( 1)    PARM( 1)

        where: NAME(J)  = label of the J'th variable/parameter,

               ISTAT(J) = 0 if the corresponding parameter should be estimated
                            freely,
                         -1 if the corresponding parameter is constrained to a
                            fixed number,
                          m if the corresponding parameter is constrained
                            to be equal to another parameter with the same
                            number m ("inter-parameter constraint").  Each m>0
                            creates a set of equality-constrained parameters.

               PARM(J)  = initialvalues of the J'th parameter,

               NPP = total number of all primary parameters = NXX + NTH + NTAU.
               (See below for the definition of "primary" parameters)

        NOTE:  The user must be careful

               - to include the correct number of initial values:
                    1) sum of all NXM(K) interactions of all NX+NXD+NXA
                       explanatory variables K (=NXX)
                    2) plus all nontrivial dissimilarity parameters (=NTH+NTAU)

               - to respect the order of the initial values:
                    1)  Coefficients of explanatory variables (BETA)
                        a)  Interactions of alternative-specific attributes
                        b)  Interactions of agent-specific characteristics
                        c)  Interactions of alternative-specific constants
                    2)  Upper-level dissimilarity parameters (level 1) (TAU)
                    3)  Lower-level dissimilarity parameters (level 2) (THETA)

        The order of the explanatory variables has to correspond to the
        order in the data file.

        NOTE: The number of initialvalues for explanatory variables (excl.
              dissimilarity parameters), NXX, has to be equal to the number of
              lines in the interaction maps.

        The order of the dissimilarity parameters is from the left to the
        right in the tree as specified in STRUCT.

        NOTE: For each non-trivial dissimilarity parameters one initial value
              must be provided.
              Trivial upper-level dissimilarity parameters are in limbs that
              have only one branch, trivial lower-level dissimilarity
              parameters are in branches that have only one alternative.  They
              do not get initialvalues.

        HLOGIT distinguishes three types of parameters that correspond
        to the three different ISTAT values (0, -1, and m>0):
        1) Parameters that are completely free (ISTAT=0).  This is the
           standard status for likelihood maximization.  On estimation, they
           are chosen to maximize the loglikelihood function.
        2) Parameters that are fixed at a given number (ISTAT=-1).
           On estimation, their value is kept fixed.
        3) Parameters that are being estimated but that are also constrained
           to be equal to some other parameter (ISTAT=m>0).  Each m>0 defines
           a set of equal parameters.  On estimation, their joint value is
           chosen to maximize the loglikelihood function.

        NOTE: These three parameter types define three parameter vectors:
        1) The vector of "primary parameters".  It includes all NPP parameters
           of type 1), 2) and 3) in the "INPARMS.PAR" file.  NP=NXX+NTAU+NTH.
        2) The vector of "free parameters".  It includes only those parameters
           that are not constrained to a fixed number, i.e., all parameters with
           ISTATò0, i.e. all parameters of type 1) and 3), counting all para-
           meters subject to inter-parameter equality constraints separatly.
        3) The vector of "deep parameters".  It includes the NP parameters
           entering the likelihood maximization.  Sets of equality-constrained
           parameters identified by a common ISTAT>0 count only once.
           Hence, NP is the number of all parameters with ISTAT=0 plus the
           number of sets of equality-constrained parameters.

-----------------------------------------------------------------------------

  2.3  DATA:  THE INPUT FILES "INDATA.DAT" and "INDATA.BIN":
  ==========================================================

     HLOGIT is intended to be addressed by an external data handling program
     that generates and manipulates the data that will be fed into HLOGIT for
     estimation and analysis.

     Data can be read in from a file with ASCII numbers or an HLOGIT binary
     file.  ASCII-files are portable, binary files are much faster
     to read and write.  HLOGIT binary files should be created by HLOGIT
     if the same data set will be used several times.

     We will first describe some generalities, then the format of an ASCII
     raw data file and an HLOGIT binary data file.

     2.3.1  SIZE OF DATA SET:
     ------------------------

     HLOGIT does not limit the number of observations.  However, if the data
     exceeds the size of the internal worksheet ("buffer"), data has to be
     moved between the HLOGIT binary scratch file and memory ("paging") which
     substantially slows the program down.

     The size of the internal worksheet to store data depends on the specific
     installation of HLOGIT.  In the standard version, the buffer is exactly
     one memory segment of 64 KBytes, corresponding to MAXBUF=16000 numbers
     (see the beginning of Chapter 3).
     The number of observations that fit in this internal worksheet depends
     on the number of alternatives (NALT), the number of explanatory variables
     (NX and NXD), and whether a weight and a choice set variable are included
     or not (NWT and NCS).  It can be computed by the formula:
        MAXOBS = MAXBUF/NDA - 2
     where the number of data items per observation is
        NDA = (NX+NCS)*NALT+1+NWT+NXD

     All data is read at the beginning of the program.  If the file is ASCII,
     the user has at this point the option of generating an HLOGIT data file
     in binary format.  The creation of this binary file is required if the
     data set does not fit into memory.

     2.3.2  VARIABLE TYPES:
     ----------------------

     Six types of variables should be distinguished (Cf. Section 1.3):
     (1) The dependent variable. For each observation, this is the index of the
         chosen alterative.  (See below for indexation.)
     (2) If NX > 0:
         NX alternative-specific explanatory variables ("attributes") which
         vary by NALT alternatives and (possibly) by observation. For each
         observation, this is a two-dimensional array of NALT rows and NX
         columns.
     (3) If NXD > 0:
         NXD agent-specific variables ("characteristics") which vary only by
         observation but not by alternative. For each observation, this is a
         row-vector of length NXD.
     (4) If NXA = 1:
         A constant term. It will be generated internally, so one must not
         include it in the data.
     (5) If NWT = 1:
         The weights. For each observation, this is a number
         carrying a weighting factor. (See below for examples.)
     (6) If NCS = 1:
         The choice set variable. For each observation, this is a column
         vector of zeroes and ones of length NALT, in which a one (zero)
         indicates that the corresponding alternative is included (excluded)
         in the observation's choice set.

     NOTE: In oder to conserve space in HLOGIT data sets, the above order of
           variables does NOT correspond to the actual order in HLOGIT data
           sets.  For the actual order, see Subsection 2.3.3 below.

     The dependent variable indicates the alternative chosen and carries a
     value between 1 and NALT, corresponding to the order in which the
     alternatives are stored.

     The weights are applied to each observation's likelihood as well as to
     summary statistics, predictions and elasticities.  They can also be
     used as replication factors for grouped data analysis since the sum
     of the weights across observations need not sum up to one.  In all
     summary statistics, HLOGIT divides by the sum of weights, not the number
     of physical observations.

     EXAMPLES:
     (1) In simple random sampling with balanced choice sets, the weights in
         each observation and alternative are 1.0.  Therefore, it is
         unnecessary to include weights in the data, set NWT=0.
     (2) In simple choice based sampling, the weights are the population share
         of the alternative chosen by the observation divided by the sample
         share of this alternative.
     (3) In stratified random sampling, the weights represent the weight of
         the corresponding stratum.
     (4) The user can combine (2) and (3).


     2.3.3  ASCII raw data files:
     ----------------------------

     The first line of the ASCII data file must be a valid REAL FORTRAN format
     description.  The format has to be enclosed in parentheses. Including the
     parentheses, the format must not exceed 72 characters.

     The program then expects NALT lines for each observation. Each 
     line carries NCS+NX+NWT+1+NXD entries in the following order using the
     above user-specified format.
     1)  1, if the corresponding alternative is included in the choice set
         of the observation,  0 else.  (Omit this entry, if NCS=0).
     2)  NX alternative-specific characteristics for the corresponding
         alternative and observation.  (Omit these entries, if NX=0).
     3)  The dependent variable (=index of the chosen alternative.  This entry
         must always be present)
     4)  The weight (Omit this entry, if NWT=0)
     5)  NXD agent-specific attributes.  (Omit these entries, if NXD=0).

     NOTE: Items 3)-5) are the same for all alternatives of an observation.

     NOTE: For each observation, the first line is read completely with the
           complete format description.  In the remaining NALT-1 lines of each
           observation, only the first NCS+NX items are read with the first
           NCS+NX items of the above format.  The index of the chosen
           alternative and the NXD agent-specific attributes are ignored,
           since they are identical to those in the first alternative.
           (Accordingly, they can also be omitted in the data file, creating a
           non-rectangular file structure).

     NOTE: If NCS+NX=0, each observation must have only one line of data.

     NOTE: The alternatives are assumed to be in ascending order independently
           of the structure of the tree that will be estimated. The dependent
           variable must be an integer between 1 and NALT corresponding
           to the alternatives in ascending order.  In other words, the index
           of each alternative is defined by the order in the data file.

     NOTE: The number and the order of alternatives must always be the same
           for each observation.  This should be emphasized in the case of
           unbalanced choice sets.  In this case, also the alternative-specific
           variables in the alternatives excluded from the choice set should
           be given some value to avoid a read error although this value will
           never be used.


     EXAMPLE: Imagine the following data for a four-alternative choice problem
              (NALT=4):

     1)  A choice set variable (assume, observation one has no alternative 3)
         (NCS=1).
     2)  Two alternative-specific attributes P ("price of alternative") and
         Q ("quality of alternative").  P should be attached with two different
         coefficients, one for alternatives 1 and 2, the other for alternatives
         3 and 4.  Q should be attached with a common coefficient in all four
         alternatives:
         (NX=2,  NXM=2, LMAP=1 1 0 0
                             0 0 1 1
                 NXM=1, LMAP=1 1 1 1)
     3)  The dependent variable (Assume, observation 1 has chosen alternative
         2 and observation 2 has chosen alternative 3)
     4)  Weights are included (assume, observation 1 has a third of the
         weight of observation 2) (NWT=1)
     5)  Three agent-specific characteristics Y,S,A ("income, household
         size, and age") which are interacted by two dummies
         (NXD=3, NXM=2, LMAP=1 0 0 0
                             0 1 1 0)
     6)  A constant which is interacted with three dummies
         (NXA=1, NXM=3, LMAP=1 0 0 0
                             0 1 0 0
                             0 0 1 0)

     The ASCII-data file should look like:     or, more economical, like:

     (F3.1,2F10.3,2F5.1,3F10.3)                (F1.0,2F9.3,F2.0,F4.1,3F9.3)
     1.0  P11  Q11  2.0  0.5  Y1  S1  A1       1 P11 Q11 2 0.5 Y1 S1 A1
     1.0  P12  Q12  2.0  0.5  Y1  S1  A1       1 P12 Q12
     0.0  P13  Q13  2.0  0.5  Y1  S1  A1       0 P13 Q13
     1.0  P14  Q14  2.0  0.5  Y1  S1  A1       1 P14 Q14
     1.0  P21  Q21  3.0  1.5  Y2  S2  A2       1 P21 Q21 3 1.5 Y2 S2 A2
     1.0  P22  Q22  3.0  1.5  Y2  S2  A2       1 P22 Q22
     1.0  P23  Q23  3.0  1.5  Y2  S2  A2       1 P23 Q23
     1.0  P24  Q24  3.0  1.5  Y2  S2  A2       1 P24 Q24
     etc.                                      etc.

     NOTE: The interaction feature will expand the explanatory variables
           internally to the following array:

           P11  0    Q11  Y1  0   S1  0   A1  0   1  0  0
           P12  0    Q12  0   Y1  0   S1  0   A1  0  1  0
           0    P13  Q13  0   Y1  0   S1  0   A1  0  0  1
           0    P14  Q14  0   0   0   0   0   0   0  0  0
           P21  0    Q21  Y2  0   S2  0   A2  0   1  0  0
           P22  0    Q22  0   Y2  0   S2  0   A2  0  1  0
           0    P23  Q23  0   Y2  0   S2  0   A2  0  0  1
           0    P24  Q24  0   0   0   0   0   0   0  0  0
           etc.

           (The PRINT DATA option -- see below, Subsection 3.11 -- will display
           the data in this expanded fashion)

     2.3.4  HLOGIT binary data files
     -------------------------------
     For speedier execution, the ASCII data file can be converted to an
     HLOGIT binary file.  This file is created by specifying the appropriate
     option in the prompt before reading the data in.  Binary data files must
     be created for data sets larger than the available workspace.

     The HLOGIT binary data files consist of NOBS vectors of
        NDA=(NCS+NX)*NALT+1+NWT+NXD
     items.  All items are stored as REAL*4 numbers.

     For each observation, the data is stacked as follows: 
     1) NALT values of the choice set variable (only if NCS=1)
     2) NALT values of the first alternative-specific explanatory variable,
         ...
        NALT values of the NX'th alternative-specific explanatory variable,
     3) 1 value of the weight (only if NWT=1)
     4) 1 value of the dependent variable,
     5) NXD values of the agent-specific variables.

     IMPORTANT NOTE:
           The binary data is written in the order as specified in the
           currently active tree structure STRUCT.  If the arrangement of
           alternatives in that tree implies a permutation of alternatives,
           the binary file will NOT carry the alternatives in ascending order
           and great care is necessary to use this data for other than the
           original tree structure.

     EXAMPLE:
     --------
     The above data would be arranged for the binary data set as follows:

     1.0 1.0 0.0 1.0  P11 P12 P13 P14  Q11 Q12 Q13 Q14  2  0.5  Y1 S1 A1
     1.0 1.0 1.0 1.0  P21 P22 P23 P24  Q21 Q22 Q23 Q24  3  1.5  Y2 S2 A2
     etc.,
     if tree 12,34 was specified while reading the raw data;

     and

     1.0 0.0 1.0 1.0  P11 P13 P12 P14  Q11 Q13 Q12 Q14  2  0.5  Y1 S1 A1
     1.0 1.0 1.0 1.0  P21 P23 P22 P24  Q21 Q23 Q22 Q24  3  1.5  Y2 S2 A2
     etc.,
     if tree 13,24 was specified while reading the raw data.

-----------------------------------------------------------------------------


  3. PROGRAM SEQUENCE, OPTIONS AND OUTPUT
  =======================================

  At the beginning, HLOGIT will display the following maximal dimensions which
  are version specific.  Consult the README file included on the distribution
  diskette.

         MAXBUF = size of internal worksheet in memory,
         MAXNP  = total number of parameters,
         MAXTH  = 1st order dissimilarity parameters at level 2,
         MAXTAU = 2nd order dissimilarity parameters at level 1,
         MAXBRA = number of branches on each limb at level 2,
         MAXLIM = number total number of limbs at level 1,
         MAXNX  = alternative specific explanatory variables,
         MAXNXD = agent specific explanatory variable,
         MAXALT = elemental alternatives.

  A fatal error will occur if one of these maximal dimensions is exceeded.

  NOTE: The internal worksheet stores as much of the data file as possible.
        HLOGIT uses additional memory for computational purposes that are
        allocated internally and depends essentially on the magnitudes
        of MAXALT and MAXNP.

  HLOGIT will then read the PROFILE.  If no profile was specified on the
  command line and the default profile HLOGIT.PRO does not exist, an error
  will occur.

  In BATCH mode the program will then execute the batch commands listed in the
     profile starting with line 12.  The batch commands correspond to the
     options listed below.  

     All batch commands have five character keywords.  The following
     conventions apply:
     1. Keywords must begin in colum 1.
     2. Keywords may be abbreviated up to minimium identificating length, see
        examples below
     3. The argument list is enclosed in parentheses.
     4. Arguments are separated by commas.
     5. Arguments must be integers or simple real variables (no exponentials).
     6. The argument list can be omitted.  In this case, the default values
        will be used.

     Examples:
     correct:               incorrect:
     --------------------   ------------------------------------------------
     ESTIM(2,.001,10)       ESTIM(2,.001,10      missing parenthesis
     ESTIM( 2 , .001 , 10)  E STIM(2,.001,10)    space in keyword
     ESTIM()                ESTIM(2,.0 01, 10)   space in number
     ESTIM                  ESTIM(2.0,1.E-3,10)  incorrect data types
     estim                  ESTIM(2,.001)        too few arguments
     ES(2,.001,10)          ESTIM(2 .001 10)     no commas between arguments
     es                     E                    too short: same as ELAST

  In INTERACTIVE mode, a menu will appear and you can choose among the
     options listed below.


  A) ESTIMATION AND STATISTICS:
  =============================


  3.1: ESTIMATION (BATCH: ESTIM / MENU: OPTION=1)
  ===============================================
  HLOGIT estimates the parameters by full information maximum likelihood.

  BATCH SYNTAX:  ESTIM(IALG,ACC,ITER) or ES [DEFAULT: ESTIM(2,.001,10)]

  INTERACTIVE MODE:  If you do not select the default iteration parameters
  specified in the HLOGIT profile, you will be prompted for:
     
     (1) The numerical optimization algorithm (argument IALG):

         1 = Method of steepest ascent.
             (Not recommended. Requires no computation of hessian, will always
             converge, but it converges very slowly.  Use only for almost
             singular problems.
             NOTE: Since the algorithm does not compute a hessian,
             standard errors and t-statistics are unusable).
         2 = Davidon-Fletcher-Powell algorithm.
             (Recommended.  Will almost always converge, does not require
             computation of hessian.  Will provide estimate of inverse hessian,
             but this estimate tends to be very poor and is not recommended for
             covariance estimate)
         3 = Newton-Raphson algorithm.
             (Requires computation of hessian.  Will not necessarily lead to 
             optimum for distant starting values.  Use if close to optimum.
             Recommended for MNL, as in this case convergence is assured)
         4 = Berndt-Hall-Hall-Hausman algorithm.
             (Recommended. Will always converge, and does not require
             computation of hessian.  Will provide estimate of hessian.  In 
             small samples this estimate may be poor)
         5 = Quadratic Hillclimbing algorithm.
             (Requires computation of hessian.  Converges in relatively few
             iterations, but each iteration very slow.  Use if collinearity
             problems stall other algorithms)
         6 = Quadratic Hillclimbing algorithm, hessian updated only every
             second iteration.
             (See 5, needs more iterations, but is more economical per
             average iteration.  On balance sometimes faster, sometimes slower
             than 5)

     (2) The accuracy for convergence criteria (argument ACC):

         There are three convergence criteria.  Whichever is satisfied first,
         determines convergence.
         1 = Relative change in parameter values between two iterations is less
             than given accuracy (may indicate a stationary point only).
         2 = Norm of gradient is less than given accuracy (convergence assured)
         3 = Relative change in function values between four iterations is less
             than given accuracy (may indicate a stationary point only).

     (2) The iteration limit (argument ITER)

         This is the inner loop of the optimization program.  If this number is
         exceeded or an exit condition (convergence, failure) is reached, the 
         optimizer returns to the outer loop asking whether additional itera-
         tions are desired and whether a new specification of the iteration
         parameters is desired.

  The iteration log includes iteration number and algorithm, the value of the
  loglikelihood function, the norm of the gradient, the inner product of gra-
  dient times whatever is used as direction vector, and the current parameter
  vector.

  NOTE: A small gradient times direction can be used as a sensible convergence
        criterion only in Newton-Raphson and BHHH iterations.
        It is meaningless in steepest ascent iterations.  In DFP, the approxi-
        mation to the hessian (and therefore gradient times direction) is bad
        unless the number of iterations is close to or exceeds the number of
        parameters to be estimated.

  IN INTERACTIVE MODE: If converged or aborted, HLOGIT prompts you for more
  iterations, possibly with a different algorithm.  If you choose to quit, you
  will be prompted for the output file name "OUTPARMS.PAR" that creates a file
  with the estimation output that can be used for later inputs.

  IN BATCH MODE: Results are written to the file specified in the profile.

  NOTE: It is recommended to employ DFP or BHHH until convergence, then
        recalculate the covariance matrix by using option 2, below, with
        analytic derivatives.

  NOTE: The output file includes (in parentheses) the following return codes:
        -9 = Hessian singular
        -8 = Eigenvalues did not converge
        -7 = Numerical saddlepoint
        -6 = Cannot find improving step
        -5 = Too many function errors
        -4 = *** Out of memory ***
        -3 = Function error in gradient evaluation
        -2 = Initial values not admissible
        -1 = Iteration limit exceeded
         0 = *** Unknown error ***
         1 = Stepsize convergence achieved
         2 = Gradient convergence achieved
         3 = Function value convergence achieved
         4 = Gradient*direction convergence achieved


  3.2: COVARIANCE MATRIX (BATCH: COVAR / MENU: OPTION=2)
  ======================================================
  This option lets you re-calculate the covariance matrix, e.g., with a
  different method of computing second derivatives, and/or prints on
  screen (punches on file) the entire covariance matrix of the parameter
  estimates.

  NOTE: If the sample is choice-based, the covariance matrix must be
        corrected in this step.


  BATCH SYNTAX: COVAR(IALG,RELSIZ,IPRINT,IPUNCH) or C [DEFAULT: COVAR(3,0,0,0)]

  INTERACTIVE MODE:  If you do not select the default input parameters,
  you will be prompted for:

  (1) Algorithm (argument IALG)
      Algorithm for calculating the hessian on which the covariance is based
      0 = no recalculation of covariance matrix
      3 = recalculation with exact hessian
      4 = recalculation with BHHH approximation of hessian

  (2) WESML Correction (argument RELSIZ)
      0.0 = simple random sampling
      1.0 = choice-based sampling with exact WESML weights
 
      NOTE: A real number different from 0.0 or 1.0 can be used as input
            for RELSIZ, if the WESML weights are not exact but estimated
            from some other external ("auxiliary") sample.  In this case,
            RELSIZ must be the ratio of number of observations in the
            auxiliary sample divided by the number of observations in the
            estimation sample.

  (3) Print Covariance Matrix on screen (argument IPRINT)
      0 = no, 1 = yes

  (4) Punch Covariance Matrix on result output file (argument IPUNCH)
      0 = no, 1 = yes


  3.3: PREDICTION (BATCH: PREDI / MENU: OPTION=3)
  ===============================================
  This option computes a prediction success table in which observed choices
  are compared to predicted choices.  (Predictions are made according to 
  maximum probability).

  Likelihood at zero parameters is related to likelihood at estimated
  parameters (McFaddens Rho: 1-LIK/LIK0), the likelihood and the implied
  utility (inclusive value at stem level, sometimes referred to as
  social surplus) at predicted choices is computed.

  Aggregate relative choice frequencies (market shares) are computed
  according to individual maximum probability prediction as well as by
  averaging over individual choice probabilities.

  The choice probabilities and the label (1-9,0,A-Z) of the predicted
  choice (maximum utility) for each observation can be punched on file.

  All statistics take weighting of observations into account.


  BATCH SYNTAX:  PREDI(IPUNCH) or PRE [DEFAULT: PREDI(0)]

  INTERACTIVE MODE: You will be prompted for

  (1) Punch predicted choices and probs on output file (argument IPUNCH)
      0 = no , 1 = yes


  3.4: ELASTICITIES (BATCH: ELAST / MENU: OPTION=4)
  =================================================
  This option computes the set of matrices of choice probability elasticities
  with respect to all exogenous variables E(i,k,j):  the elasticity of
  choice probability i with respect to how variable k is set in alternative j.

  Two methods to compute these elasticities are different due to the non-
  linearity of the NMNL model:
  (1) The elasticity is evaluated at sample means and frequencies (quick, but
      aggregation-biased)
  (2) The elasticities are evaluated at each observation and then averaged
      (slower, but consistent)

  All elasticities take weighting of observations into account.

  NOTE: If E(i,k,j)=0 for all choice probabilities i and all observations,
        this row of elasticities is not printed out.  For example, this is the
        case for elasticities referring to explanatory variables that are zero,
        in particular for the zero case of variables interacted with dummy
        variables.


  BATCH SYNTAX:  ELAST(IMODE) or EL [DEFAULT: ELAST(0)]

  INTERACTIVE MODE: You will be prompted for

  (1) Computation of elasticities (argument IMODE)
      0 = evaluation only at sample means and frequencies
      1 = average of evaluation at each observation
      2 = both


  3.5: TREE STRUCTURE TEST STATISTICS (BATCH: TESTS / MENU: OPTION=5)
  ===================================================================
  The significance of the tree-structured NMNL model versus the unstructured
  MNL model can be tested by comparing the likelihood values.  This option
  computes the other two (asymptotically equivalent) statistics of the
  test trinity: Wald and Lagrange statistic.  Null hypothesis is MNL
  (i.e., all dissimilarity parameters are one).  Degrees of freedom are
  displayed for the chi-squared statistics.

  NOTE: This option yields sensible results only if either preceeded by a
        successful estimation with reliable standard errors (Option 1, ESTIM)
        or preceeded by the recalculation of the covariance matrix (Option 2,
        COVAR).  Also, the proper initial values must be present depending on
        the test, see below.


  BATCH SYNTAX:  TESTS(ITEST) or T [DEFAULT: TESTS(0)]
                 

  INTERACTIVE MODE: You will be prompted for

  (1) Test (argument ITEST)
      0 = Wald test [DEFAULT]
      1 = Lagrange multiplier test

      It is important to make sure that the initial values are correctly
      specified:
      
      Wald test:
         The initial values must be NMNL estimates with estimated dissimilarity
         parameters.  The tree structure must be active, i.e., include commas
         and/or semicolons.
         The covariance matrix must be present.  This is the case AFTER
         successful NMNL estimation.

      Lagrange multiplier test:
         The initial values must be MNL estimates with unity dissimilarity
         parameters added to the parameter input file.  The tree structure must
         be active, i.e., include commas and/or semicolons.
         The covariance matrix must be present.  This is the case BEFORE NMNL
         estimation, but after a COVAR call.

      EXAMPLE:
         Assume an IMPARMS parameter file with MNL estimates.  Activate the
         tree structure, i.e., include commas and/or semicolons as appropriate.
         Append the corresponding number of dissimilarity parameters with unit
         starting values.  Then running the following commands:
            COVAR
            TEST(1)
            ESTIM
            TEST(0)
         will produce the correct Lagrange multiplier and Wald tests, provided
         that the estimation step was successful.  Of course, subtracting the
         initial loglikelihood from the loglikelihood after estimation, and
         multiplying this difference by two, yields the usual likelihood ratio
         statistic.

  3.6: IMPLIED CORRELATION MATRIX (BATCH: ICORR / MENU: OPTION=6)
  ===============================================================
  Each NMNL model (tree structure) implies a covariance matrix of the unob-
  served utility components in the random utility maximization model where
  the correlations depend in an factor-like way on common limbs and
  common branches in the tree.  This option computes the full covariance
  matrix of the unobserved utility components, and normalizes it by taking
  differences with respect to the last alternative and by scaling the
  covariance matrix so that the lower right variance is unity.  In general,
  this variance is not unity (e.g., ã/û3 for MNL). The scaling factor 
  is the square root of the lower right variance of the pre-scaled normalized
  covariance matrix.  All parameter estimates should be multiplied
  by this factor to be comparable to probit estimates with unit variance.

  BATCH SYNTAX:  ICORR() or I

  INTERACTIVE MODE:  No prompt.


  3.7: SIMULATION OF FINITE CHANGES (BATCH: SIMUL / MENU: OPTION=7)
  =================================================================
  Simulates finite changes of one agent-specific variable while all other
  variables are held constant.  Two sets of choice probabilities and their
  differences are evaluated at two user-specified values of the variable in
  question and contrasted with the choice probabilities at sample means.
  This option provides a discrete alternative to elasticities (OPTION=4)
  which are often meaningless in the case of dummy variables.

  BATCH SYNTAX:  SIMUL(IXVAR,IMODE,VAL1,VAL2) or S [DEFAULT: SIMUL(1,2,0,1)]

  INTERACTIVE MODE:  You will be prompted for

  (1) Index of variable to be changed (argument IXVAR)
      This index must be between 1 and NXD.

  (2) Change and evaluation mode (argument IMODE)

      1 = change evaluated AT MEAN of all variables except changed variable,
          change RELATIVE to mean of changed variable,

      2 = change evaluated AT MEAN of all variables except changed variable,
          ABSOLUTE change between two values specified below

      3 = AVERAGE INDIVIDUAL change after evaluation of all observations at
          original value of all variables except changed variable,
          change RELATIVE to mean of changed variable

      4 = AVERAGE INDIVIDUAL change after evaluation of all observations at
          original value of all variables except changed variable,
          ABSOLUTE change between two values specified below

  (3) First value of variable to be changed (argument VAL1)
      If RELATIVE change, this is the fraction
         - of the average value of the variable to be changed
           (if change evaluated at mean)
         - of each observations's value of the variable to be changed
           (if average individual change)
      If ABSOLUTE change, this is the absolute value to be inserted
         - as average value of the variable to be changed
           (if change evaluated at mean)
         - for each observation as value of the variable to be changed
           (if average individual change)

  (4) Second value of variable to be changed (argument VAL2)
      Same as VAL1 above for the second evaluation

  Examples:  SIMUL(1,1,0.95,1.05)  will compute:
             - choice probabilities evaluated at sample means except agent-spec.
               variable No.1, which is set to 5 percent below the sample mean,
             - choice probabilities evaluated at sample means except agent-spec.
               variable No.1, which is set to 5 percent above the sample mean,
             - the differences between these two sets of choice probabilities.

             SIMUL(2,4,0.0,1.0)  will compute:
             - average choice probabilities at sample variables except agent-
               spec. variable No.2, which is set to 0.0 at all observations
             - average choice probabilities at sample variables except agent-
               spec. variable No.2, which is set to 1.0 at all observations
             - the differences between these two sets of choice probabilities.

             SIMUL() will compute:
             - choice probabilities evaluated at sample means except agent-spec.
               variable No.1, which is set to 0.0
             - choice probabilities evaluated at sample means except agent-spec.
               variable No.1, which is set to 1.0
             - the differences between these two sets of choice probabilities.


  B) UTILITIES
  ============


  3.11: PRINT DATA (BATCH: PRINT / MENU: OPTION=11)
  =================================================
  Allows you to check data observation by observation.  Displays data in
  expanded form, i.e., with all interactions applied.  See the example at the
  end of Subsection 2.3.3.

  BATCH SYNTAX:  PRINT(IOBS1,IOBS2) or PRI [DEFAULT: PRINT(1,1)]

  INTERACTIVE MODE:  You will be prompted for

  (1) First observation to be printed (argument IOBS1)
  (2) Last observation to be printed (argument IOBS2)


  3.12: SPOOL STATUS (MENU: OPTION=12)
  ====================================
  Turns spooling of output on file on/off, and changes the length of the pause
  between screens of terminal output.  Note that specifying a length longer
  than 60 seconds will turn on a prompt between screens of output.

  BATCH SYNTAX:  This command is not available in batch mode.

  INTERACTIVE MODE:  You will be prompted for

  (1) Spool Status
      0 = no spooling of output
      1 = spooling of terminal output on file

  (2) Pause Status
      0 = no pause between screens of output
      1-59 = pause in seconds
      60 = prompt between screens of output


  3.13: DERIVATIVE CHECK (BATCH: DERIV / MENU: OPTION=13)
  =======================================================
  Compares analytical and numerical derivatives.  Should be accurate up to
  4 digits unless when close to optimum (zero gradient).  If the derivatives
  do not check, there is an error in the likelihood function and/or derivative
  routine.  Please report.

  BATCH SYNTAX:  DERIV(IMODE) or D  [DEFAULT: PREDI(1)]

  INTERACTIVE MODE:  You will be prompted for

  (1) Comparison of derivatives (argument IMODE)
      1 = check of first derivatives only
      3 = also check of exact hessian
      4 = also check of BHHH hessian 


  3.99: QUIT HLOGIT (BATCH: QUITT / MENU: OPTION=99)
  =======================================================
  Quit the program and return to operating system.

  BATCH SYNTAX:  QUITT() or Q


------------------------------------------------------------------------------


  3.20: FILES READ OR WRITTEN BY HLOGIT WITH FORTRAN UNIT NUMBERS
  ===============================================================

  INPUT FILES:

     "HLOGIT.PRO":   FT18   Profile
     "INPARMS.PAR":  FT20   Tree structure and initialvalues.
     "INDATA.DAT":   FT07   ASCII data file.
     "INDATA.BIN":   FT08   Binary data file.

  OUTPUT FILES:

     "HLOGIT.OUT":   FT10   Spool file in which terminal output is
                            copied (OPTIONAL).

     "OUTPARMS.PAR": FT19   Tree structure and estimation results. 
              This file can be used as new tree input file 20. 
              Parts A) through C) are copied from "INPARMS.PAR";
              in Part D), the initialvalues are replaced
              by the estimated parameters, incl. standard-errors and t-
              statistics. Appended are summary-statistics.

              NOTE:
              T-statistics are evaluated for the null-hypothesis
              that the corresponding parameter is 0, EXCEPT for the
              dissimilarity parameters, where the null-hypothesis is that
              the corresponding dissimilarity parameter is 1, the MNL-case.

     "COVMAT.OUT":   FT09   Echo of the covariance matrix on file (OPTIONAL).

     "PREDIC.OUT":   FT09   Data file of predicted choices (OPTIONAL).

     The terminal will prompt you for file names, except for the profile file
     which is taken from the command line (or HLOGIT.PRO if omitted). If the
     output files already exist, they will be overwritten (after a prompt in
     interactive mode, always in batch mode).  If you enter blank names, the
     default names from the PROFILE will be used.

----------------------------------------------------------------------------

  4.  A SIMPLE NMNL TEST PROCEDURE:
  =================================

     Use the following bootstrapping procedure to generate data to test the
     NMNL estimation results.  In the most simple trinary NMNL model
          _
         / \
        /  /\

     the following exogenous variables and parameter values:

        x = (0,0,1) for all observations
        á = log2 = 0.6931471806
        é = 0.5

     will create the following choice probabilities:

        p1 = 0.30902
        p2 = 0.13820
        p3 = 0.55279.

     A large data set in which the endogenous variable reflects these choice
     probabilities will reproduce the above parameter values.  For smaller
     data sets, some bias will occur due to the integer constraint on choice
     frequencies.

     EXAMPLE ( n=50 => n1=15, n2=7, n3=28):

     NMNL ==> lik=-48.05730, a'=0.729822, e'=0.52645
                             (ao=.2747)   (ao=.2213)
                             (t=2.657)   (t=-2.140, measured around 1.0)

     MNL  ==> lik=-49.54573, a'=0.93433 , e':=1.0

-----------------------------------------------------------------------------

     INPARMS file for the above example:

     full three-level code      quick two-level code      simple MNL-code
     ---------------------      --------------------      ------------------
     12;3                       12,3                      123
     1,0,0,0,0                  1,0,0,0,0                 1,0,0,0,0
     1   1,1,1                  1   1,1,1                 1   1,1,1
     BETA.... 0     0.0         BETA.... 0     0.0        BETA.... 0     0.0
     TAU..... 0     1.0         THETA... 0     1.0

------------------------------------------------------------------------------

     5. MACHINE-SPECIFIC CONSTANTS AND HINTS FOR PORTING HLOGIT
     ==========================================================

     DUPP is largest argument for exponentation
     DLOW is smallest number for denominator/logarithm

     HARDWARE:           SOFTWARE:                DUPP:     DLOW:
     ------------------  -----------------      --------   --------
     PRIME-MINICOMPUTER  F77                    22622.D0   1.D-9824
     IBM MAINFRAME       CMS VSFORTRAN            173.D0   1.D-74
     IBM-COMPATIBLE PC   MICROSOFT FORTRAN 5.0    708.D0   1.D-307
     IBM-COMPATIBLE PC   WATFOR-77/87             708.D0   1.D-307

     Some routines are specific for IBM-PC under DOS 3.2 and above.
     This is in particular the routine PROFILE which uses a DOS system
     call to retrieve command line arguments, and SNOOZE and TSTAMP which
     call the DOS system clock.
     The routines PULL and TRANS handle the transfer of data.  If the buffer
     exceeds one memory segment (64KBytes=16000 REAL*4 numbers) the compiler
     has to use far rather than near addresses in this routine (e.g., by using
     the $LARGE metacommand).

------------------------------------------------------------------------------